SECTION 629 - PAVEMENT MARKINGS

Make the following amendments to said Section:

(I)	Amend Subsection 629.03(B) – Temporary Pavement Markings by revising the third paragraph from line 62 to 63 to read:

“Maintain and replace temporary pavement markings, flexible delineators, and barricades.  ”

(II)	Amend Table 629.03 – 1 – Temporary Pavement Markings to read as follows:

| “TABLE 629.03-1 TEMPORARY PAVEMENT MARKINGS |
| --- |
| TYPE | PAVEMENT MARKINGS |
| Passing Permitted - Both Sides | Single 4-inch yellow stripe 5 feet in length spaced 20 feet on center with Type D markers spaced 40 feet on center and located on center of 5-foot length of stripe. |
| Passing Prohibited - Both Sides | Double solid 4-inch yellow stripes with Type D markers placed 20 feet on center on one of 4-inch yellow stripes selected by the Engineer. |
| Passing Permitted - One Side Only | Single continuous 4-inch yellow stripe with Type D markers placed on stripe 20 feet on center on no-passing side and single 4-inch yellow stripes 5 feet in length spaced 20 feet on center on passing side. |
| Lane Lines - Lane Changing Permitted | Single 4-inch yellow or white stripe 5 feet in length spaced 20 feet on center with Type C or Type D markers spaced 40 feet on center. |
| Lane Lines - Lane Changing Prohibited | Double solid 4-inch white stripes with Type C markers placed 20 feet on center on one of the 4-inch white stripes selected by the Engineer. |
| Crosswalk | Two 12-inch white transverse lines spaced 8 feet on center or as ordered by the Engineer. |
| Stop Line | Single 12-inch white transverse line. |
| Note: Paint may be used for temporary markings in areas where final paving is not complete.” |

# END OF SECTION 629