Amend Section 207 - Ditch and Channel Excavation to read as follows:

“SECTION 207 - DITCH AND CHANNEL EXCAVATION

207.01	Description.     This work includes excavating highway ditches and water channels above and below culverts and bridges,  including channels for changing the course of streams according to the contract.     This work does not include ditches within the normal cross section of the roadway.

207.02	Materials.     None specified.

207.03	Construction Requirements.     Notify the Engineer ten working days before excavating ditches and channels.

Use suitable materials from ditch and channel excavation in the construction of embankments and dikes.     Unsuitable and surplus excavation material shall become the Contractor's property.     Dispose the unsuitable and surplus material at no cost to the State.

Backfill and compact excavation below the required bottom grade of ditches and channels with suitable material according to the contract at no cost to the State.

Remove debris and unwanted material from the excavated ditches and channels before acceptance.

207.04	Method of Measurement.     When ditch and channel excavation is paid for per cubic yard,  the Engineer will measure ditch and channel excavation per cubic yard in accordance with the contract documents.     When ditch and channel excavation is paid on a lump sum basis,  measurement for payment will not apply.

207.05	Basis of Payment.     The Engineer will pay for the accepted pay items listed below at the contract price per unit,  as shown in the proposal schedule.     Payment will be full compensation for the work prescribed in this section and the contract documents.

The Engineer will pay for the following pay items when included in the proposal schedule:

## Pay Item	Pay Unit

### Ditch and Channel Excavation	Cubic Yard

The Engineer will pay for:

(1)	80 percent after clearing and grubbing,  excavating ditch,  and backfilling and compacting below the required bottom grade of ditches and channels.

(2)	20 percent of the contract bid price upon completion of disposing the unsuitable and surplus material

### Ditch and Channel Excavation	Lump Sum”

# END OF SECTION 207