SECTION 503 - CONCRETE STRUCTURES

Make the following amendments to said Section:

(I)   Amend 503.04     Method of Measurement to read as follows:

"503.04     Method of Measurement.     The Engineer will measure the concrete per cubic yard in accordance with the contract documents.

The Engineer will not make deductions for the volume occupied by the reinforcing steel, piles, floor drains, weepholes,  timber bumpers,  pipes less than 8 inches,  conduits,  or expansion joint materials.

The Engineer will consider the wingwalls to be a part of the structure.

(II)	Amend 503.05     Basis of Payment to read as follows:

"503.05     Basis of Payment.     The Engineer will pay for the accepted concrete at the contract unit price per cubic yard.     Payment will be full compensation for the work prescribed in this section and the contract documents

The Engineer will pay for the following pay item when included in the proposal schedule:

## Pay Item	Pay Unit

Concrete ______________(Class _____ if applicable) 	Cubic Yard

The Engineer will pay for:

- 20 percent of the contract bid price upon completion of furnishing and installing falsework,  formwork,  and centering;

- 60 percent of the contract bid price upon completion of placing ,  curing,  and finishing the concrete;  placing construction and expansion joints;  waterproofing and applying joint sealer.

(3)	20 percent of the contract bid price upon completion of removing the falsework and forms;  and cleaning up.

The Engineer will pay for reinforcing steel in accordance with Section 602 - Reinforcing Steel.

# END OF SECTION 503