## SECTION 602 - REINFORCING STEEL

Make the following amendments to said Section:

(I)	Amend 602.07      Method of Measurement and 602.08     Basis of Payment to read as follows:

“602.07	Method of Measurement.     Reinforcing steel will be paid on a lumps sum basis.     Measurement for payment does not apply.

The Engineer will base the weights calculated according to Table 602-III.

| TABLE 602-III - BAR DESIGNATION, WEIGHT, AND AREA |
| --- |
| Bar No. | Weight Per Linear Foot (Pounds) | Area (Square Inches) |
| 3 | 0.376 | 0.11 |
| 4 | 0.668 | 0.20 |
| 5 | 1.043 | 0.31 |
| 6 | 1.502 | 0.44 |
| 7 | 2.044 | 0.60 |
| 8 | 2.670 | 0.79 |
| 9 | 3.400 | 1.00 |
| 10 | 4.303 | 1.27 |
| 11 | 5.313 | 1.56 |
| 14S | 7.650 | 2.25 |
| 18S | 13.600 | 4.00 |

The Engineer will not make allowance for clips,  wire or other material used for fastening reinforcement in place.

The Engineer will not measure mesh reinforcement.

602.08	Basis of Payment.     The Engineer will pay for the accepted reinforcing steel on a contract lump sum basis.     Payment will be full compensation for the work prescribed in this section and the contract documents.

The Engineer will pay for the following pay item when included in the proposal schedule:

Pay Item	Pay Unit

Reinforcing Steel for __________________	Lump Sum

The Engineer will not pay for mesh reinforcement separately and will consider the cost for mesh reinforcement as included in the contract prices for the various contract pay items.     The cost is for the work prescribed in this section and the contract documents”

# END OF SECTION 602