## SECTION 625 - SEWER SYSTEM

Make the following amendments to said Section:

(I)	Amend the first paragraph of 625.02  Materials by adding the following:

"Cullet Materials for Utility Structures	717.03

Cullet Materials for Drainage Systems	717.04"

(II)	Amend the second paragraph of 625.02 Materials to read as follows:

“Concrete for sewage structures shall conform to Section 601 - Structural Concrete.     Modify the concrete in contact with sewage or sewage gases as follows:

(1)	By incorporating a water reducing admixture conforming to Subsection 711.03(B) - Water Reducing Admixtures.

(2)	By using Type II Portland Cement or a modified Type I Portland Cement with a maximum limit of 8% on tricalcium aluminate.

Concrete for non-reinforced concrete blocks,  cradles and jackets shall be Class C.

Concrete for reinforced concrete blocks,  cradles and jackets shall be Class B.”

(III)	Amend 625.04     Method of Measurement to read as follows:

“625.04	Method of Measurement.     The pay items listed below will be paid on a lump sum basis.     Measurement for payment will not apply.”

(IV)	Amend 625.05     Basis of Payment to read as follows:

“625.05	Basis of Payment.     The Engineer will pay for the accepted pay items listed below on a contract lump sum basis,  as shown in the proposal schedule.     Payment will be full compensation for the work prescribed in this section and the contract documents.

The Engineer will pay for each of the following pay items when included in the proposal schedule:

Pay Item	Pay Unit

_____ - Inch, _____ Sewer Pipe	Lump Sum

### Sewer Laterals	Lump Sum

Cast Iron Fittings (_________)	Lump Sum

Extending 6-Inch Sewer Laterals	Lump Sum

Chimneys	Lump Sum

_____ - Inch, Wye	Lump Sum

_____ - Inch, Bend	Lump Sum

_____ Reducer with Cap	Lump Sum

Marker	Lump Sum

__________ Concrete Cradle for _____ - Inch (________ Pipe)	Lump Sum

__________ Concrete Jacket for _____ - Inch (________ Pipe)	Lump Sum

Bed Course Material for Crushed Rock Cradle	Lump Sum

_____ - Inch, Drop Connection at Sewer Manhole	Lump Sum

_____ - Inch, Shallow Drop Connection at Sewer Manhole 	Lump Sum

House Sewer Connection	Lump Sum

Instead of the above payments, could we go (as long as the plan identifies what sewer systems work must be done)?:

### Sewer Systems	Lump Sum

The Engineer will pay for excavation and backfill for sewer pipes under Section 206A – Excavation and Backfill for Miscellaneous Facilities.

The Engineer will not pay separately for concrete blocks,  cutting and plugging of abandoned sewers,  concrete plugs for ends of abandoned sewers,  and vitrified clay caps at ends of existing sewers that will remain in use.     The Engineer will consider the cost for these items as included in the contract prices for the various sewer system contract pay items.”

# END OF SECTION 625