Make the following Section a part of the Standard Specification:

“SECTION 636 – FIELD OFFICE AND

PROJECT SITE LABORATORY TRAILER

636.01	Description.     This section describes furnishing,  placing,  maintaining and subsequently removing portable,  weatherproof trailer(s) used exclusively by the Project Engineer as a field office and a project site laboratory.

636.02	Materials.     Furnish and install new material necessary to complete this work.

636.03	Construction Requirements.

(A)		General.     The field office trailer and project site laboratory trailer provided shall conform to the contract documents and as directed by the Engineer.

(1)	Within 10 days after a contract is awarded,  submit catalog cuts,  shop drawings,   or both for the Engineer’s acceptance.

(2)	The Engineer will determine the exact location of the trailer in the field.     Place the trailer(s) within two weeks after the Engineer determines the location in the field.

(3)	The Engineer and its staff will have exclusive use of the trailer(s) and area surrounding the trailer(s) within 30 feet of the outer most edges of the trailer.     If there are two or more trailers,  the distance shall be 30 feet from a square or rectangle formed by the outer limits of the trailer.     The trailer(s) will be separated from any buildings used by the Contractor and not share any utilities.     Construct an 8-feet high chain link fence with barbed wire and a double swing gate entrance with each gate having a width of 15 feet.     Maintain a clearance of 30 feet minimum from the building,  ramp,  walkway,  and stairs.     The Engineer will determine the exact location of the fence.     Remove the fencing and restore area after the completion of the project or removal of field office/project laboratory complex.

(4)	Comply with all local laws,  ordinances, rules, and regulations pertaining to the placing of the trailer(s) and their appurtenances and shall obtain necessary permits and licenses and publish or post notices required.     The Contractor shall comply with local laws,  ordinances,  rules,  and regulations pertaining to the placing of the trailer(s) and their appurtenances and its construction even if it is exempt.     Unless the exemption is in relation to the obtaining the necessary permits and licenses and publishing or posting of notices to which the Engineer may allow the exemption.

(5)	Furnish and install the required pipes and appurtenances,  including a water main,  to connect to the closest County Sewer main and water supply system.     Connect the pipes according to the plumbing ordinances of the appropriate County and State Department of Health.

(6)	Provide a combination surface mounted,  weatherproof or raintight meter socket panel designated for single phase 3-wire solid neutral 120/240 volt service with a 4-jaw meter socket

1 – 100 amp. main breaker

1 - 20 amp. breaker 2/pole

6  - 20 amp. breaker single pole

(7)	Maintain the trailer(s),  surrounding ground of the trailer(s),  furnishings,  appliances,  and other equipment in good order and provide rubbish pickup service twice a week for a period not to exceed 90 calendar days beyond the date of final acceptance of the completed project by the State.     Employees of the State of Hawaii or their consultants may use the field office trailer and project site laboratory trailer at no increase in contract price or contract time to the other Contractors.

(8)	The trailer(s) and furnishings shall become the property of the Contractor upon completion of the project.     Remove the trailer(s) within 7 calendar days from the end of the 90-day period specified above or earlier upon receipt of written notice from the Engineer.

(9)	Provide and maintain a separate ADA compliant toilet facility for each trailer (8-feet x 4-feet minimum) which shall include a door and screened window.     The toilet facility shall have a flush type toilet and wash basin with running water and all related plumbing fixtures necessary.     The room shall have two lights.     One light shall be inside the room and one light shall be outside the room.     Both lights shall be connected to one switch and shall be able to turn on both lights at the same time.     The toilet facility shall be for the exclusive use of the State.

(10)	Clean the site of the trailer(s) and leave the site in a clean and presentable condition after removal of the trailer(s).     Restore the area such as any grass or pavement to the same or better condition than it originally was.

(11)	Furnish and install covered and lighted six-foot wide walkways with non-slip surfaces for the length of the trailer.     If two or more trailers are provided,  the covered and lighted walkway shall connect all the trailers.     All exterior doors shall have a heavy-duty dead bolt lock,  which is opened by a key from the outside and a lever or knob from the inside.     In addition to the heavy-duty dead bolt lock,  all exterior and interior doors shall have a separate ADA compliant heavy-duty cylindrical lever handle entrance lock which shall have an outside deadlocking latch bolt operated by a key and a pushing turn button.     Locks for the trailer(s) shall be keyed alike, i.e., one key can open all doors.     Provide 10 sets of keys for each trailer.

(12)	Provide the trailer(s) with concrete hollow tile foundation and steps, four telephones,  potable water,  sewage disposal,  electrical lighting (fluorescent) with an illumination of not less than 50-foot candles,  central air conditioner units of not less than 30,000 BTU rating each,  five exterior flood lights on a timer and two fire extinguishers per trailer as specified by the Engineer.     The telephones shall be key telephone set type with two separate lines per trailer.

(13)	Provide metal security screens over all trailer windows.     Security screens shall be galvanized expanded metal sheet, 9 gauge, welded to an angle iron frame welded to the trailer.     Security screens shall be galvanized prior to installation.     All welded points shall be regalvanized.

(14)	Provide a monitored alarm system and fire alarm system that detects smoke and heat for the field office and project site laboratory trailers.     If more than one trailer is provided the alarm system shall have one key pad in each trailer to set the alarms and shall be able to set the alarm for all the trailers from each key pad.     All perimeter openings and interior space shall be protected     Coordinate contact person for alarm with the Engineer prior to installation.

(B)		Field Office.     The Contractor shall furnish a 12 feet x 56 feet trailer meeting the requirements specified in the contract documents.

Submit to the Engineer a plan or brochure for acceptance of the field office trailer.     The Engineer shall determine the layout for the trailer facility including toilet.

(C)	Project Site Laboratory.     The Contractor shall furnish a 10 feet x 24 feet trailer meeting the requirements specified in the contract documents.

Submit to the Engineer a plan or brochure for acceptance of the project site laboratory trailer.     The Engineer shall determine the layout for the trailer facility including toilet.

(D)	Field Office Trailer Furnishings.     The Contractor shall provide the following items for each of the field office(s):

(1)	Two file cabinets, metal with lock 4-drawer legal-size, 18 inch W x 26 inch D x 52 inch H.

(2)	One steel double pedestal executive with lock, dimensioned and equipped as follows, or similar:

(a)	60 inches long by 30 inches wide.

(b)	Three box drawers on left pedestal and one box drawer and one file drawer on right pedestal.

(3)	Two steel double pedestal compact administrative desks with lock, dimensioned and equipped as follows, or similar:

(a)	54 inches by 24 inches wide.

(b)	One box drawer and one file drawer at each pedestal.

(4)	Three portable work tables,  72 inch L x 30 inch W x 29 inch H.

(5)	Three executive swivel chair with arm rests and capable of adjusting the tension and height.     The padded areas shall be at least 2-1/2 inches thick.     Chairs shall be on five canisters.

(6)	One engineering draftsman stool with adjustable seat height up to 6 inches and backrest height up to 3-3/8 inches and a chrome foot ring or similar.

(7)	Four stackable chairs steel framed.

(8)  One aluminum framed bulletin board 38 inches wide by 36 inches high.

(9)	One aluminum framed white porcelain enamel steel board 48 inches wide by 36 inches high with full length marker rail and a dry erase marker.

(10)	One aluminum plan rack 25 inches long by 18 inches wide by 48 inches high.

(E)	Project Site Laboratory Trailer Furnishings:     The Contractor shall provide the following items for the project site laboratory.

(1)	Two each steel double pedestal compact administrative desks with lock, dimensioned and equipped as follows,  or similar:

(a)	54 inches long by 24 inches wide

(b)	One box drawer and one file drawer at each pedestal.

(2)	One each portable work table (72 inch L x 30 inch W x 29 inch H)

(3)	One each electric stove with oven

(4)	One each metal storage cabinet (6 feet H x 3 feet W) 2-door with lock

(5)	Two each 4-drawer legal-size locking metal file cabinets (18 inch W x 26 inch D x 52 inch H).

(F)	Maintenance of Trailers.     The force account work includes the monthly utility charges (but not the initial installation,  start up charges for the utilities,  or the disconnection of utilities);  maintaining the trailer and surrounding ground of the trailers;  maintaining the furnishings,  appliances,  and other equipment in good order,  treating the ground under the buildings for termites; providing rubbish pickup service twice a week;  providing and maintaining the toilet facility;  providing janitorial services for both buildings;  relocating the buildings if necessary; and as ordered by the Engineer.

Site restoration shall be at no increase in contract price and contract time.

636.04	Method of Measurement.

(A)	The Engineer will measure maintenance of trailers on a force account basis in accordance with Subsection 109.04 – Payment for Additional and Force Account Work and as ordered by the Engineer.

(B)	Field office trailer and project site Laboratory trailer will be paid on a lump sum basis.     Measurement for payment will not apply.

636.05	Basis of Payment.     The Engineer will pay for the accepted pay items listed below contract price per pay unit,  as shown in the proposal schedule.     Payment will be full compensation for the work prescribed in this section and the contract documents.

The Engineer will pay for each of the following pay items when included in the proposal schedule:

Pay Item	Pay Unit

### Maintenance of Trailers 	Force Account

An estimated amount for the force account may be allocated in the proposal schedule under ‘Maintenance of Trailer’,  but the actual amount to be paid will be the sum shown on the accepted force account records,  whether this sum be more or less than the estimated amount allocated in the proposal schedule.

Field Office Trailer (Not to Exceed $32,000.00)	Lump Sum

Project Site Laboratory Trailer (Not to Exceed $22,000.00)	Lump Sum

The contract lump sum amount for the field office trailer and the project site laboratory trailer also includes the initial utility cost and the disconnection of utilities.

The maximum bids allowable for the field office and project site laboratory are $32,000 and $22,000 respectively.     If the proposal submitted by the bidder indicates an amount in excess of the allowable maximum for either or both items, the indicated amount or the amounts shall be reduced to the allowable maximum, as appropriate.     The 'Sum of All Items' in the proposal schedule shall be adjusted to reflect any such reduction.     For the purposes of comparing bids and determining the contract price to be inserted in the contract awarded to the bidder, if so awarded, the 'Sum of All Items' adjusted according to the foregoing shall be used and the bidder's proposal shall be deemed to have been submitted for the amounts as reduced and adjusted in accordance herewith.”

# END OF SECTION 636

# Comments

(Provide allowance of $8,000/year per trailer)

FYI

Field Office Trailer				Lease Price - $485/month

Purchase Price - $44,000

Project Site Laboratory Trailer		Lease Price- $450/month

Purchase Price - $29,000