SECTION 706 - CONCRETE, CLAY, AND PLASTIC (PVC) PIPE

Make the following amendment to said Section:

(I)	Amend the title to read as follows:

"SECTION 706 - CONCRETE, CLAY, AND PLASTIC PIPE"

(II)	Add the following:

"706.10	High Density Polyethylene Pipe.

(A)		High Density Polyethylene Pipe for Drainage System.     This pipe shall conform to AASHTO M 252 or M 294 Type C or Type S.     Submit a certificate of compliance to the Engineer before using any plastic pipe.

(B)		Couplings.     Couplings shall be of the same composition as the pipe."

END OF SECTION 706