## SECTION 712 - MISCELLANEOUS

Make the following amendments to said Section:

(I)	Amend 712.37 Controller Equipment to read as follows:

"712.37	Controller Equipment.

(A)		Controller Assembly.	Controller Assembly shall consist of a Model 170 Controller,  Cabinet,  and Auxiliary Equipment.     Except where noted,  only manufacturers and products listed on the current State of California,  ‘Qualified Products List (QPL) for Model 170 Controller Assembly,’  from the California Department of Transportation (CALTRANS) shall be acceptable.     A copy of the latest QPL is available from  the City &  County of Honolulu,  DTS,  Phone (808) 527-6988.

The Contractor should review Section 623.03(G)(2)(a) concerning quality control and testing prior to field installation.

For this project,  Controller Assemblies are described and supplied as follows:

(1)		Type 170'  Controller Assembly and  Model  332  Controller Cabinet shall mean the latest Model 170 Controller Assembly and Model 332 Controller Cabinet on the most current CALTRANS Qualified Products List (QPL).

(2)		Each Controller Assembly shall contain the sufficient amount of items listed below for a full 8 vehicle,  4 pedestrian and 4 preemption phase intersection,  even though the plans does not reflect it.

Item	Quantity

Model 170 Controller	2

Model 412C Prom Module	2

Model 400  Modem	2

332A Aluminum  Cabinet	1

Model 200  Load  Switches	12

Model 204  Flasher	All

Model 242  Isolators	2

Model FS/ST  Isolator	All

Flash Transfer  Relays	All

Model 210  Conflict  Monitor	1

Model 262C  Detector  Amplifiers  (Rotary Sw Type)	8

Model M752 Preempt.  Car  (Non-QPL)	2

Model UTS  (Non-QPL)	1

(B)	Model  170  Controller.     	Each  Model  170  Controller  shall  meet the following additional requirements:

(1)	Model 412C Prom Module includes a 27256 EPROM Chip

(2)	A Supercap replaces the battery as the standby power supply to keep the DTA and  RAM on the CPU board powered for at least 8 hours during ac power loss.

(3)	Dual ACIAs,  C2 and C20,  serial communication ports.

(4)	All Controller Boards mounted vertically.

(5)	One Manual with each controller.

(6)	Documented Validation Testing according to CALTRANS test specifications.

(C)		Cabinet.     Each 332A Cabinet shall meet the following additional requirements:

(1)	Minimum Wired for 8 vehicle phases,  4  pedestrian phases,  and 4 preemption phases.

(2)	Cabinets fabricated from 0.125 anodized Aluminum.

(3)	Cabinet's Main Breakers shall be rated as 50 amps.

(4)	Entire Output File copper hard-wire of sufficient gauge to withstand current surges before circuit breakers or surge protectors trip.

(5)	A LED Display for Modem Transmit,  Receive,  and Carrier Detect status will be clearly visible after opening the cabinet's front door. Attach indicators mounted on a 0.75 Inch by 2.0 Inch aluminum assembly to the top center of the cabinet's rack.     Indicators will derive their signals from the C2 ACIA.     Bundle the wire with a protective jacket.

(6)	C2 Terminal Blocks protected from current surges by EDCO PC642 or equal.

(7)	Input File and Field Terminal Blocks wired for 3M M752  Opticom Priority Module EVA,  EVB,  EVC,  and EVD.

(8)	Front and back fluorescent lights activated upon opening any door.

(9)	Convenience  GFI  Receptacles.

(10)	Door locks of solid  brass rim Best Lock Series 516RL3XA7559-606 and include 2 keys.

(11)	Labeling by Silk-Screening  only.

(12)	Output File Terminal Blocks labeled in reference to its assigned phase and signal indications.

(13)	Attach One Each 24.0 inch by 36.0 inch Cabinet Print in a weatherproof plastic jacket to front and back cabinet doors.

(14)	Documented validation testing of cabinet and conflict monitor iaccording to CALTRANS  test specifications.

(D)		Auxiliary  Equipment.     The Contractor shall deliver the controller unit supplied with the following auxiliary equipment:

Auxiliary equipment not on the QPL shall meet the following pertinent 	requirements:

(1)	Model M752 Optical Preemption Module.     The M752 will be card-type and will interface with the Model 170 cabinet preemption slots of the input file.     Each M752 Module will have 2 channels of preemption.     The M752 will include firmware to discriminate between  the two valid priority signals,  to prioritize valid same priority signals on a first come basis,  and to override the low priority signal if a high priority is received.     The M752 Module will receive input signals (9.639 and 14.035 hz) to permit priority preemption operation within the 170 local intersection program.     M752 will optically isolate output signals and will trigger an active low signal to the controller for high priority and a pulsed active low signal for low priority.     All new preemption equipment will be a 3M Opticom System.

(2)	Universal Time Standard (UTS) Module.     The UTS Module will be a stand alone precision clock located in the Controller Cabinet which shall update the internal clock of the Model 170 controller by decoding Five Broadcast Frequencies (2.5,  5,  10,  15,  20 Mhz)  transmitted by WWVH of the U.S. National Institute of Standards and Technology.     All hardware and software of the UTS equipment will be compatible without any modification to the Model 170 Hardware or Software.     The UTS Module shall have the following specifications:

1.5 ms Time Accuracy;  2 - 4 Minutes Time to Acquire; Minimum  5 - Frequency,  AM,  Crystal-Controllered,  Dual Conversion,  Superheterodyne Receiver;  Automatic Scan 5 Frequencies;  Data Output  RS-232C,  1200 & 2400 Baud rate,  No Parity,  8 Data Bits,  1 Stop Bit;  One Hour Selectable Time Zones: Daylight Saving Time Option;  24 Hour Time Format;  Month,  Day, and Year Date;  DB25-RS232 and BNC Antenna Connector;  DB25 to Model 170 C2 cable and Connectors;  2-foot outdoor Whip Antenna with Pole Adapter Bracket;  100 linear feet of RG-58  Coaxial Cable with Connectors;  Approximate Size 1.5 Inch H x 8 Inch W x 9 Inch D and Weight 1.5 Lbs.;  24  VDC;  Traconex / Multisonics UTS Model 1010 or equal.     All UTS equipment and antennas will be installed by the Contractor and included in the controller assembly bid."

# END OF SUBSECTION 712.37