SECTION 712 - MISCELLANEOUS

Make the following amendment to said Section:

(I)	Amend 712.06(B)     Pullboxes to read as follows:

"(B)	Pullboxes.     Pullboxes installed in shall be constructed of polymer concrete and reinforced by heavy weave fiberglass.     Dimensions shall be per plans.     Logo on skid resistant, non-locking cover shall read “TRAFFIC”, ELECTRIC” or “TELEPHONE”, per plans.     Pullboxes shall have a minimum H20 AASHTO load rating.”

# END OF SECTION 712