Make the following Section a part of the Standard Specifications:

“SECTION 151 - CONTRACTOR QUALITY CONTROL

151.01	Description.    This work consists of obtaining and performing tests for Contractor quality control testing, performing tests for Contractor process control, providing inspection, and exercising management control to ensure that work conforms to the contract requirements.

151.02	Contractor Quality Control Plan.     The Contractor is responsible for all process control sampling and testing.     A written Control Quality Plan shall be submitted to the Engineer at the pre-construction conference.      The plan should include sampling and testing frequencies and the use of control charts to monitor production.     Do not begin the work until the Quality Control Plan covering that work is approved by the Engineer.     With prior approval, submission of a Quality Control Plan for items of work not immediately scheduled to begin may be deferred.

Submit the following with the Quality Control Plan:

(A)		Process Control Testing.     List the material to be tested, tests to be conducted, the location of sampling, and the frequency of testing.

(B)		Inspection/Control Procedures.     Address each of the following subjects in each phase of construction:

(1)	Preparatory Phase.

(a)	Review all contract requirements.

(b)	Ensure compliance of component material to the contract requirements.

(c)	Coordinate all submittals including certifications.

(d)	Ensure capability of equipment and personnel to comply with the contract requirements.

(e)	Ensure preliminary testing is accomplished.

(f)	Coordinate surveying and staking of the work.

(2)	Start-Up Phase.

(a)	Review the contract requirements with personnel who will perform the work.

(b)	Inspect start-up of work.

(c)	Establish standards of workmanship.

(d)	Provide on-the-job training.

(e)	Establish detailed testing scheduled based on the production schedule.

(3)	Production Phase.

(a)	Conduct intermittent or continuous inspection during construction to identify and correct deficiencies.

(b)	Inspect completed phases before scheduled Engineer acceptance.

(c)	Provide feedback and system changes to prevent repeated deficiencies.

(C)		Description of Records.     List the records to be maintained.

(D)		Personnel Qualifications.     The Contractor shall provide sufficient numbers of qualified personnel to perform all required sampling and testing as required by the contract provisions.     The Contractor shall furnish to the Engineer the name, authority, relevant experience, and qualifications of the person with overall responsibility for the Contractor inspection system.

(E)		Subcontractors.     Include the work of all Subcontractors.     If a Subcontractor is to perform work under this Section, detail how that Subcontractor will interface with the Contractor’s and/or other Subcontractor’s organization.

Modifications or additions may be required to any part of the plan that is not adequately covered.     Supplement the plan as work progresses and whenever quality control or quality control personnel changes are made. Approval of the Quality Control Plan will be based on the inclusion of the required information.     Approval does not imply any warranty by the Engineer that the plan will result in consistent contract compliance.     It remains the responsibility of the Contractor to demonstrate such compliance.

151.03	Control Chart and Record Keeping.     The Contractor shall maintain control charts for all items requiring Contractor acceptance testing.     The control chart shall identify the following:

Project number;

Contract item number;

Test parameter(s);

Upper and/or lower specification limit for each test parameter;

Test results.

Control chart format shall be approved by the Engineer.     The Contractor shall keep the charts current and post them in a location satisfactory to the Engineer.     The Contractor shall use the control charts as part of a process control plan for identifying production and equipment problems and for identifying pay factor reductions before they occur.

The Contractor is responsible to maintain complete testing and inspection records and make them available to the Engineer.     For each day of work, the Contractor shall prepare an ‘Inspector’s Daily Record of Construction Operations’ (Form FHWA 1413) or an approved alternate form.     The form shall include the following certification signed by the person with overall responsibility for the Contractor inspection system:

‘It is hereby certified that the information contained in this record is accurate,  and that all work documented herein complies with the requirements of the contract.     Any exceptions to this certification are documented as a part of this record.’

Submit the record and certification to the Engineer within one working day of the work being performed.     If the record is incomplete, in error, or otherwise misleading, a copy of the record will be returned to the Contractor with corrections noted.     When chronic or missions occur, the Contractor is responsible to correct the procedures by which the records are produced.

151.04	Acceptance.     The Contractor’s quality control will be accepted under Subsection 106.16 - Contractor Inspection System.     If the Engineer’s acceptance testing and inspections indicate that the Contractor’s quality control system to correct these deficiencies, and furnish notification in writing to the Engineer of improvements and modification to the system.

151.05	Method of Measurement.     The Engineer will not measure for the Contractor quality control for payment.

151.06	Basis of Payment.     The Engineer will not pay for the Contractor quality control separately.     The Engineer will consider the cost for the Contractor quality control as included in the contract price of the various contract items.

The cost is for obtaining samples; performing Contractor quality control testing; performing tests for Contractor quality control testing; performing tests for Contractor process control; providing inspection;  exercising management control;  submitting a written Control Quality Plan, maintaining control charts; submitting the records and certifications; and furnishing labor, materials, tools, equipment, and incidentals necessary to complete the work.

# END OF SECTION