SECTION 603 – CULVERTS AND STORM DRAINS

Make the following amendment to said Section:

(I) Amend Subsection 603.03 (C)(1) Culverts, by revising lines 106 to 108 to read as follows:

“Spacing between multi-barrel culverts shall be a minimum of 18 inches or 0.5 the culvert width, whichever is greater.  The minimum spacing shall be 1 foot when placing controlled low strength material (CLSM) as backfill. Anchor the culverts in such a manner that the horizontal and vertical alignment of the culverts does not change.”

# END OF SECTION 603