SECTION 619 – PLANTING

Make the following amendments to said Section:

(I)	Amend Subsection 619.02(H)(3) – Application Records from lines 207 to 210 to read:

“(3)  Application Records.  Records shall be kept by Contractor of dates of application, type of fertilizer or manure used, quantities, and areas that were covered and shall be submitted to Engineer within 24 hours of application.  Document if rates and amounts of fertilizer deviate from manufacturer’s specifications.”

(II)	Amend Subsection 619.03(A) – Codes and Standards from lines 262 to 264 to read:

“(A)	Quality Assurance.

(1)	Codes and Standards.  Perform work in accordance with applicable laws, codes, and regulations.  Provide inspections and permits required by Federal, State, and local governmental authorities.

(2)	Qualifications.  To become qualified in the work class of Landscaping, the applicant shall provide a letter containing the following:

- A statement declaring at least five continuous years of experience of a scope similar to that required for the work, including installing temporary irrigation (where applicable), hydro-mulch application, soil preparation, and plant installation and establishment.

- The letter must be signed and dated by the Owner of the Company or Company Officer.

- Produce a list of completed projects similar to the scope and size of the required work to substantiate the experience.  The list shall contain a minimum of five different landscape projects, excluding single-family residential landscape.  A minimum of five different landscape projects shall be rated positive on a performance evaluation by the references in the list below.  Names and references must be current and verifiable.  Use separate sheets of paper that contain all of the following information:

- Project name

- Location of project (city, state)

- Owner

- Owner Contact (name and current phone number)

- Architect or Engineer Company Name

- Architect or Engineer Contact (name and current phone number)

- Construction Manager (name and current phone number)

- Description of Project, Scope of Work Performed

- Total Value of Construction (including change orders)

- Original Scheduled Completion Date

- Actual Date of Completion

(d)	Approval.  The Contractor shall submit the items under this section to the Engineer for approval prior to construction.  If the applicant does not have proof of five continuous years of experience with a minimum of five completed projects similar in scope and size, the Contractor shall remove the applicant from the project upon receipt of a written notice from the Engineer. Requests to substitute an applicant will be allowed under Subsection 105.16 Subcontracts.”

(III)	Amend Subsection 619.03(I)(1) – Adding Fertilizer and Amendments by revising the section from lines 310 to 314 to read:

“(1)  Uniformly distribute fertilizer and amendments over planting areas as recommended by the Soil Analysis Report as specified in Section 617 – Planting Soil.  Document if rates and amounts of fertilizer deviate from manufacturer’s specifications.  Rototill top four inches of soil to evenly incorporate fertilizer and amendments.  Rototill before installing drip irrigation system.”

(IV)	Amend Subsection 619.03(T)(3) – Fertilizing by adding the following paragraph after line 478:

“Submit recommendations from a licensed Landscape Architect when deviating from the application rates and amounts above.  Document if the rates and amounts of fertilizer deviate from manufacturer’s specifications.”

# END OF SECTION 619