SECTION 415 – COLD PLANING OF EXISTING PAVEMENT

Make the following amendments to said Sections:

(I)	Amend Section 415.04     Measurement, from line 67 to 68 to read as follows:

“415.04 	Measurement.

(A)	Cold Planing will be paid on a lump sum basis.     Measurement for payment will not apply.

(B)	The Engineer will measure cold planing per square yard in accordance with the contract documents.”

(II)	Amend Section 415.05 Payment, from line 70 to 79 to read as follows:

“415.05 	Payment.     The Engineer will pay for the accepted pay items listed below at the contract price per pay unit, as shown in the proposal schedule.     Payment will be full compensation for the work prescribed in this section and the contract documents.

The Engineer will pay for one of the following pay items when included in the proposal schedule:

Pay Item	Pay Unit

(A)	Cold Planing	Lump Sum

(B)	Cold Planing	Square Yard

(1)	80 percent of the contract bid price upon completion of removing the indicated thickness and clean and sweep before opening to public traffic;

(2)	20 percent of the contract bid price upon completion of removing the material and disposing of the removed material.”

# END OF SECTION 415

# Comments

Use lump sum if the project is quantifiable and plans are well defined. Otherwise use ton. The State or County Design Engineer has a final say also based on the nature of the work item, and the project or scope of work.