SECTION 613 – CENTERLINE AND REFERENCE SURVEY MONUMENTS

Make the following amendments to said Section:

(I)	Amend Subsection 613.03(A) – Initial Installation from lines 22 to 26 to read:

“(A)	Initial Installation.     Cut holes, in completed medians and shoulders,  to required depth or to solid rock, whichever is less.     Fill hole with concrete.     Burr or feather plug for anchorage in concrete.     Place the 4 #4 x 20-inch bars as shown on the plans when curing the concrete.     Install brass plug in required position after concrete has sufficiently set.     After curing concrete at least 7 days, restore edge of pavement surrounding monument to original condition.”

(II)	Amend lines 58 through 60 of Subsection 613.04 - Measurement to read as follows:

"(C)	Adjusting Centerline and Reference Survey Monument.  The Engineer will measure for adjustments of centerline and reference survey monuments on a force account basis in accordance with Subsection 109.06 - Force Account Provisions and Compensation and as ordered by the Engineer.

(D)	Survey Work.  Survey work to verify the centerline and reference survey monuments will be paid on a lump sum basis.  Measurement for payment will not apply."

(III)	Amend lines 71 through 87 of Subsection 613.05 - Payment to read as follows:

"(C)	Adjusting Centerline and Reference Survey Monument.  The Engineer will pay for the accepted adjustments of centerline and reference survey monuments on a force account basis in accordance with Subsection 109.06 - Force Account Provisions and Compensation.  Payment will be full compensation for the work prescribed in this section and the contract documents.

(D)	Survey Work.  The Engineer will pay for the accepted survey work to verify the centerline and reference survey monuments on a contract lump sum basis.  Payment will be full compensation for work prescribed in the contract documents.”

The Engineer will pay for each of the following pay items when included in the proposal schedule:

Pay Item		Pay Unit

Centerline and Reference Survey Monuments	Lump Sum

Reconstructing Centerline and Reference Survey Monuments	Lump Sum

Adjusting Centerline and Reference Survey Monuments	Force Account

Survey for Centerline and Reference Survey Monuments	Lump Sum”

END OF SECTION 613