Amend Section 615 - Leveling Surfaces to read as follows:

SECTION 208 - LEVELING SURFACES

208.01	Description.     This work includes removing irregularities in the natural ground surface within or immediately next to the highway right-of-way.     Work done under this section shall be exclusive of the clearing,  grubbing and final clean-up operations required in other parts of this contract.

208.02	Materials.     None specified.

208.03	Construction Requirements.     The areas to be leveled or flattened shall be as specified by the Engineer.     Remove irregularities in the natural ground surface of the designated areas.     Use a power-propelled, pneumatic-tired motor grader.     Supplement by hand labor where required.  The surface to be leveled or flattened shall provide a surface over which a person may operate the power mowers.

208.04	Method of Measurement.     The Engineer will measure leveling surfaces on a force account basis in accordance with Subsection 109.04 – Force Account Provisions and Compensation and as ordered by the Engineer.

208.05	Basis of Payment.     The Engineer will pay for the accepted leveling surfaces on a force account basis in accordance with Subsection 109.04 - Force Account Provisions and Compensation.

Payment will be full compensation for the work prescribed in this section,  by the Engineer ,  and the contract documents.

The Engineer will pay for the following pay item when included in the proposal schedule:

Pay Item	Pay Unit

Leveling Surfaces	Force Account

An estimated amount may be allocated in the proposal schedule under ‘Leveling Surfaces’,  but the actual amount to be paid will be the sum shown on the accepted force account records,  whether this sum be more or less than the estimated amount allocated in the proposal schedule.

# END OF SECTION 208