SECTION 602 - REINFORCING STEEL

Make the following amendments to said Section:

(I)	Amend 602.07      Method of Measurement and 602.08     Basis of Payment to read as follows:

“602.07	Method of Measurement.     The Engineer will not measure reinforcing steel for payment.

The Engineer will base the weights calculated according to Table 602-III.

TABLE 602-III - BAR DESIGNATION, WEIGHT, AND AREA

Bar No.

Weight Per Linear Foot

(Pounds)

Area

| (Square Inches) |
| --- |
| 3 | 0.376 | 0.11 |
| 4 | 0.668 | 0.20 |
| 5 | 1.043 | 0.31 |
| 6 | 1.502 | 0.44 |
| 7 | 2.044 | 0.60 |
| 8 | 2.670 | 0.79 |
| 9 | 3.400 | 1.00 |
| 10 | 4.303 | 1.27 |
| 11 | 5.313 | 1.56 |
| 14S | 7.650 | 2.25 |
| 18S | 13.600 | 4.00 |

The Engineer will not make allowance for clips, wire or other material used for fastening reinforcement in place.

The Engineer will not measure mesh reinforcement.

602.08	Basis of Payment.     The Engineer will not pay for reinforcing steel separately and .     The Engineer will consider the cost for reinforcing steel as included in the contract prices of the various contract pay items.     The cost is for the work prescribed in this section and the contract documents.

The cost shall be for furnishing and testing sample splices and completed splices cut from rebars placed in the work, including replacing or resplicing rebars to the length shown in the contract; furnishing access facilities to permit the  Engineer to do the tests,  and for losses or delays to the Contractor resulting from the sampling and testing specified herein; and furnishing labor,  equipment,  materials,  tools and incidentals necessary to complete the work.

The Engineer will not pay for mesh reinforcement separately and.     The Engineer will consider the cost for mesh reinforcement as included in the bid contract prices of the various contract items.”

END OF SECTION 602