.Amend Section 619 - Planting and Transplanting to read as follows:

“SECTION 619 - PLANTING AND TRANSPLANTING

619.01	Description.     This work includes furnishing and planting trees, shrubs, and vines at specified locations according to the contract.

This work also includes transplanting certain designated trees to new locations according to the contract.

619.02	Materials.     Materials shall conform to the following:

Planting Soil	712.17

Commercial Fertilizer	712.18(A)

Manure	712.18(B)

Stakes, Guy Wires, Turnbuckles, and Markers	712.19

Mulch and Soil Amendments	712.45

The species and size of trees, shrubs, and vines will be the type shown in the contract or as ordered.

(A)		Plant Names.     Trees, shrubs, and vines furnished under this item shall be true to name.     The trees, shrubs, and vines shall follow standard names as adopted by the American Joint Committee on Horticultural Nomenclature and Special Publication No. 50,  ‘In Gardens of Hawaii,’ published by the B. P. Bishop Museum.

(B)		Form and Shape of Plants.     Trees, shrubs, and vines shall be nursery grown stock, strong, healthy, clean, well grown, and free from insects, diseases or rodents.     The trees, shrubs, and vines shall have average or normal, well-developed branch systems, with vigorous root systems.     Plants shall be free from disfiguring knots and abrasions of bark or other objectionable disfigurements.     The Engineer will not permit thin, weak plants.

(C)		Collected Stock.     When the contract specifies ‘collected’, the collected stock shall not be nursery grown.     They shall have grown under natural conditions at secured locations.

(D)		Ball and Burlap.     When the contract specifies ‘B&B’, ball and burlap the plants according to the contract.     Wrap the ball carefully and firmly.     When the contract uses a figure in parentheses following ‘B&B’, this confirms the diameter of the minimum sized ball that the Engineer will accept.     Handle these plants by the ball only and not by the plant itself. The slightest indication of manufactured earth balls or handling of the plant itself will be cause for rejection of the plants.

(E)		Size of Plants.     The figures shown in the proposal are the minimum and maximum heights of the plants.     When the contract uses such figures with the spread, the figures then are the minimum and maximum spreads of the plants.

The height of plant shall be the vertical measurement of plant from the ground upward as the species stand in its natural position in the nursery.  The measurements shall not include the fine or slender terminal leader, twig, or branch growth.     They shall stop where the main parts of the plant ends. The measurements of leggy plants shall be between and including the smallest and greatest dimension specified.

The spread, when specified, shall be the horizontal measurement of the plant as the species stands in its natural position in the nursery.     The measurements shall not include the fine or slender terminal shoots.  Measure each plant both in its smallest and greatest dimension and averaged.     The smallest dimension shall not be less than 60% of the greatest dimension.

619.03	Construction Requirements.

(A)		Advanced Preparation of Planting Areas.     Upon written notice from the Engineer, prepare the planting areas.     Clear the area of weeds, brush, rocks or other objectionable materials within a five-foot radius of each tree, shrub or vine.     Clearing of weeds and brush includes removing of the unwanted plants roots systems.     Grade the planting areas to plan elevation before planting.

Add a two- inch layer of soil amendment for shrubs, vines, and ground cover planting areas.     Till the soil amendment into the soil to a depth of not less than 6 inches until the soil is loose and fine textured.     The soil shall be free from stones greater than 0.5 inch in diameter.

The Engineer may eliminate soil amendment for slopes steeper than 3:1 if the Engineer decides the slope is steep to till.

(B)		Planting Time.     Do not plant if the weather or other conditions does not permit.

(C)		Plant and Tree Holes.     The diameter of each hole shall be at least four feet larger than the trunk of the tree at ground level.     The trunk of the tree need not be greater than the dimensions of the root system plus one foot.     The depth of the hole shall be large enough to contain the ball of the root system plus specified planting soil and manure.     In subsoil condition, increase the tree or plant hole diameter and depth according to the contract. Such increase will not be more than one foot of the required diameter and depth.

If encountered, the Contractor shall break up coral, rock, or hard pan to a depth of not less than 12 inches below the normal depth of the hole.

(D)		Planting.

(1)	General.     Do not order the materials until after excavating and preparing the tree or plant holes.     The actual planting operations shall proceed without delay to avoid undue evaporation and drying of roots while exposed to the air.

Prune bruised or broken roots with a clean cut at the time of planting.

Trees shall stand about three to four inches deeper and shrubs and vines shall stand about two inches deeper than the plants stood in the nursery or collecting field after settlement of the backfill.

Plant trees and shrubs plumb.     Only experienced workers shall plant and transplant.

After planting the trees and shrubs, spade or till a two feet wide area outside the pit 8 inches deep around the plants.     Keep the planting soil separate from subsoil.     Before backfilling, render the planting soil loose and friable.     Backfill mix for trees and shrubs includes one part soil amendment, one- part- manure and three parts soil by volume.

Planting shall be complete by the end of contract time.

Form earth saucers or water basins at least four inches in depth below the existing ground and equal in diameter to the plant pit around individual plants.     When planting in prepared shrub beds, form the earth saucers or water basins around the perimeter of each shrub bed.

(2)	Plants in Containers.     Before removing trees, shrubs, and vine from containers and before planting, place the trees, shrubs, and vines in their relative positions shown in the contract.     Upon acceptance, then plant the trees, shrubs, and vines in their permanent positions.     Carefully remove the plants from the containers so as not to disturb the root systems.

(3)	Plants With Exposed Roots.     After firming the soil in the bottom of the hole and placing the plant in the proper position, work the loose, friable planting soil around the roots and firm thoroughly at intervals during the process of backfilling.     Do not bruise or break the roots when tamping or firming the soil about the plants.

Do not include sticks, sod, clods, or other material that would form large air pockets in the soil in the backfill.     The Contractor may use sod near the bottom of the pit or excavation if thoroughly broken into small pieces when placing the plant or tree.

(4)	Balled and Burlapped Plants.     Handle and place balled and burlapped plants in the holes so that the soil of the ball is not loosened.     After partly backfilling the hole and firming the soil thoroughly under and around the ball, cut the burlap away from the upper half of the ball and roll back.     Adjust the remaining burlap to prevent the formation of air pockets.     Then complete backfilling and tamping to avoid loosening the soil in the root ball.

(5)	Pruning of Plants.     Prune the plants according to the contract.

Shade trees with heavy tops shall have about one-third to one-half of the growth removed by accepted methods.     Prune them to preserve the natural character of the plant.     Remove broken or badly bruised branches with a clean cut.     Paint cut surfaces over two inches in diameter with an accepted standard pruning compound.

An experienced pruner shall prune the material properly and systematically after planting stock.     Prune by the process of thinning to maintain and preserve the characteristic shape or natural form of the material.     Dispose of the material removed by pruning according to the contract.

(6)	Surplus Excavated Material.     Scatter and level off surplus material from subsoil excavations made for tree pits and holes for shrubs and vines.     Break up lumps fine to leave a neat, smooth appearance.     When the subsoil cannot blend readily with the surface soil of the planting areas, remove and dispose of the material within the highway right-of-way as specified by the Engineer.

(7)	Watering.     Water the plants the same day of planting.   Apply water in a moderate stream until the backfill soil around and below the roots or ball of earth around the roots of each plant is thoroughly saturated.     After the first watering, water the plants as often and in sufficient amount as conditions may require.

When installing a sprinkler system, the Contractor may use and operate such system.     Maintain the system and pay for the water used during the period of maintenance.

Watering equipment shall be of a type that will not cause damage to the planted area or its surroundings.     Correct the water systems that cause erosion or runoff and deemed unacceptable.     If the planted area or its surrounding erodes due to the watering method, immediately remove the runoff material and restore the area to the original grade and condition.

(8)	Planting Period.     Replace plants that fail to develop a healthy growth or destroyed during a 90-day planting period.

Water, cultivate, weed, prune, and apply pesticide, if required, to the plants for not less than 90-days after completion of planting in designated areas.

Weeding is when removing undesirable plants and their root systems, except nut grass.

Apply fertilizer at the following rates at the time of planting and again at 40 to 50 days after planting:

(a)	Trees  0.25 pound per inch diameter of trunk.

(b)	Shrubs and vines 0.25 pound per plant.

The Contractor shall place:

(a)	mulch material over pit or saucer areas of individual trees or shrubs

(b)	over the entire area of shrub beds

(c)	to a depth of at least four inches and

(d)	within two weeks after planting.

When attaining satisfactory growth before 90 days, the Contractor may submit a written request to the Engineer requesting for an earlier end to the planting period.

(9)	Staking and Guying.     Guy the trees over six feet high securely in three directions with zinc-coated steel wire of the gage specified.     Prevent the guy wires from cutting into the trunk by placing lumber or other non-cutting material around the trunk before fastening the guy wires to the tree.     Drive wood stakes 18 inches into firm ground.     Drive iron pipe or reinforcing steel stakes 30 inches into firm ground.     Keep guy wires and supports in place until the tree can support itself.

(10)	Windbreaks.     Build windbreaks for trees less than 8 feet high.     Place windbreaks on the side of the tree toward the prevailing wind.     Windbreaks include a wooden frame forming two panels at right angles to each other with the angle projecting into the wind. Drive the uprights of these frames securely into the ground.     Then cover the frame with a protective material such as palm leaves or sacking.

Each frame includes three wood posts approximately two inches by three inches in size and eight feet long.     Drive the frame so the windbreak shall be approximately 6 feet high and each panel shall be 4 feet wide.     Fasten the posts with horizontal wooden battens, one inch by three inches in size.     Fasten the posts at the top of the posts and near the ground.     Lumber need not be new, but shall be sound and free of objectionable color.

(11)	Cleaning After Planting.     Remove empty containers and debris accumulating from planting from the project when completing the planting.

(12)	Transplanting Existing Trees.     The contract will designate existing trees to be transplanted.     Remove and dispose of trees not designated for transplanting or not left in place according to Section 201 - Clearing and Grubbing.

The applicable requirements for planting shall also apply to transplanting.

Remove a tree with a ball of soil at the roots at least two feet larger than the trunk of the tree on each side at ground level.     The trunk of the tree need not be greater than the dimensions of the root system plus one foot.

Transplant trees immediately into holes large enough to contain the root system of the tree plus specified planting soil and manure.

Coat the cut section of exposed roots with a moist paste of a standard, acceptable hormone for the stimulation of new root growth before removing the tree.     Place a mixture 0.5 manure to 0.5 topsoil in the bottom of each hole except coconut trees.     Sprinkle the holes for coconut trees evenly with Chilean nitrate potash or an equal formula at the rate of four to five pounds per tree.

(E)		Plant Establishment.     Only State and Federal projects require a plant establishment period.     A plant establishment period is when the Contractor takes care of the planted area for 9 acceptable months from the accepted completion date of the planting period.     When provided for in the contract, this period may be shorter or longer depending on the type of plant or unusual conditions.

During the plant establishment period, the Contractor shall water, fertilize, cultivate, weed, prune, and apply pesticide,  if required.     When injuring, damaging, destroying, or failing to develop healthy plants, replace those plants.     Remove the dead or unsatisfactory plants promptly from the project.     Complete the replacement within two weeks after notice that the plant is not acceptable.

Besides the applications during the planting period, apply fertilizer at least three times during the plant establishment period at intervals not closer than 2.5 months at the rate of:

(a)	Trees - one-third pound per inch diameter of trunk

(b)	Shrubs and vines - one-third pound per plant.

Remove and dispose of surplus earth, papers, trash and debris that accumulates in the planted areas.     Care for the planted areas so to present a neat and clean condition.

The Engineer will credit plant establishment days to the Contractor when the Contractor does the planted area according to the contract even if not doing work daily.

The Engineer will not credit plant establishment days to the Engineer when the Contractor fails to do plant establishment work adequately according to the contract.

(F)		Acceptance.     The Engineer will decide the acceptability of the plant material furnished and planted as specified when the establishment or planting period ends, whichever is later.     Employ means to preserve the plants in a healthy growing condition.     The Engineer will hold a semi-final inspection to decide the acceptability of the plant material 90 days before the end of the plant establishment period.

When there is no plant establishment period, the Engineer will hold a final inspection when the planting period ends.     Replace dead and unsatisfactory plants in kind or quantity and size with live healthy plants installed as originally specified.     Use alternate or substitute varieties of plants only if accepted by the Engineer.

For projects with a plant establishment period, the Engineer will hold a final inspection of plant material 90 days after completing the replacement planting.

(Use This For Payment By Each)

619.04	Method of Measurement.     The Engineer will measure treesTrees, shrubs, and vines will be paid on a lump sum basis.per each complete in place.     Measurement for payment will not apply.

619.05	Basis of Payment.     The Engineer will pay for the accepted trees,  shrubs,  and  vines on a at the contract lump sum basis. unit price per each of the various species and sizes.     Payment will be full compensation for the work prescribed in this section and the contract documents.

The price includes full compensation for clearing and grading the planting areas; preparing the planting areas; watering; planting and transplanting; adding soil amendments; furnishing plants; placing and/or planting materials; establishing the plants; and furnishing equipment,  materials,  tools,  labor,  and incidentals necessary to complete the work.

The Engineer will pay for the following items when included in the proposal schedule:make payment under:

Pay Item				Pay Unit

Planting Trees (Named Type and Size),  (Species),  _____ High	EachLump Sum

Transplanted Tree (Named Type)	Lump Sum

Planting Shrubs (Named Type and Size),  (Species),  _____ High	EachLump Sum

Planting Vines (Named Type and Size),  (Species),  _____ Long	EachLump Sum

Transplanting (Species)			Each

(A)		Partial Payment Schedule For Planting Period Only.     The Engineer will pay for:

(1)	40% of the contract bid price upon completion of planting; and

(2)	60% of the contract bid price upon completion of the planting period; or

(BA)		Partial Payment Schedule For Planting Period With Plant Establishment Period.     The Engineer will pay for:

(1)	60% of the contract bid price upon completion of planting;

(2)	15% of the contract bid price in three monthly payments of 5% for satisfactory progress during the planting period;

(3)	20% of the contract bid price in 8 monthly payments of 2-1/2% for satisfactory progress during the plant establishment period;

(4)	5% of the contract bid price at final acceptance of the plant establishment period.

The Engineer will pay for planting soil according to in accordance with Section 617 - Planting Soil.”

END OF SECTION 619