## SECTION 624 - WATER SYSTEM

Make the following amendment to said Section:

(I)	Amend 624.03 (A)     General by revising the fourth paragraph to read as follows:

“Invert grades of water mains and service laterals shall provide the following minimum cover requirements from top of pipe to finish grades:

(1)	Pavement areas: Minimum  3 feet, sleeve or concrete jacket for 6 inch or larger water mains;

(2)	Under ditches: Minimum 2 feet, 1-foot if paved;

(3)	All other areas: Minimum 3-foot cover;

(4)	The highway utility encroachment committed may reduce the 3-foot minimum clearance specified above to two feet if ground conditions are ascertained to be rocky material, provided the utility lines do not encroach into the pavement structure.

(5)	The minimum cover of utility service lines under sidewalk areas and areas adjacent to the right-of-way (outside of shoulder and pavement areas) shall be one-foot six inches.”

(II)	Amend 624.03(B)(1)     General by revising the 11th paragraph to read as follows:

“The Contractor shall excavate the trenches to a depth of 6 inches below the invert grade shown in the contract, except as provided above for concrete encased mains.     The Engineer reserves the right to eliminate the 6 inches of excavation below the invert grade and the right to raise or lower the invert grade or to change the alignment.”

(III)	Amend 624.04     Method of Measurement to read as follows:

“624.04	Method of Measurement.     The pay items listed below will be paid on a lump sum basis.     Measurement for payment will not apply.”

(IV)	Amend 624.05     Basis of Payment to read as follows:

“624.05	Basis of Payment.     The Engineer will pay for accepted pay items listed below on a contract lump sum basis as shown in the proposal schedule.     Payment will be full compensation for the work prescribed in this section and the contract documents.

The Engineer will pay for each of the following pay items when included in the proposal schedule:

Pay Item	Pay Unit

_______ - Inch Ductile Iron Pipe (Class _____)	Lump Sum

_______ - Inch Concrete Cylinder Pipe (Class _____)  	Lump Sum

_______ - Inch Gate Valve (Class _____)	Lump Sum

_______ - Inch Bevel Geared Gate Valve (Class _____)	Lump Sum

_______ - Inch Spur Geared Gate Valve (Class _____)	  Lump Sum

_______ - Inch Butterfly Valve (Class _____)	Lump Sum

_______ - Inch Air Relief Valve

(_____ psi Minimum Working Pressure)	Lump Sum

_______ - Inch Split Butt Strap	Lump Sum

Hub Clamp for _____ - Inch Cast Iron Pipe

including Strong Back, Bolts, and Nuts	Lump Sum

_______ - Inch Service Clamp with

Tap for Appropriate Size Corporation Stop	Lump Sum

_______ - Inch x _____ - Inch Tapping Sleeve

including _____ - Inch Tapping Valve (Class _____)	Lump Sum

_______ - Inch x _____ - Inch Tapping Sleeve

including _____ - Inch Bevel Geared Tapping Valve (Class _____)	Lump Sum

_______ - Inch Concrete Cylinder Bend

(_____ Deg to _____Deg Inclusive) (Class _____)	Lump Sum

_______ - Inch Concrete Cylinder Pipe Nipple

(Class _____) Spigot and Plain End (_______) Long	Lump Sum

Ductile Iron Fittings (_________)	Lump Sum

(_____ - Feet) Height Fire Hydrant (_____)	Lump Sum

Fire Hydrant Curb Guard	Lump Sum

_____ - Inch _______________ Pipe	Lump Sum

___ - Inch x ___ - Inch

Blow-off Tee, ___ - Inch to fit Cast Iron Pipe	Lump Sum

_____ - Inch Removable

____ Tapped for _____ - Inch Pipe Thread	Lump Sum

_____ - Inch x _____ - Inch Concrete Cylinder

Eccentric Reducer (_____ - Inch Bell and _____ - Inch Reducer)	Lump Sum

Valve Marker		Lump Sum

Type _____ Meter Box	Lump Sum

Steel Pipe Hanger for _____ - Inch Cast Iron Pipe	Lump Sum

_____ - Inch Copper Service Laterals with

Type _____ Copper Service Connections and All Appurtenances	Lump Sum

_____ - Inch Copper Service Lateral with

Type _____ Copper Service Connection and All Appurtenances off

(_____ Main) (_________)	Lump Sum

Removing, Cleaning, and Returning of _______	Lump Sum

Instead of the above payments, could we go with Water Systems (as long as the plan identifies what water systems work must be done)?:

### Water Systems	Lump Sum

The Engineer will pay for:

(A)	Excavation and backfill under Section 206A – Excavation and Backfill for Miscellaneous Structures.

(B)	Concrete in reaction blocks, test blocks, jackets, and reaction beams under Section 503 – Concrete Structures.

- Reinforcing steel under Section 602 – Reinforcing Steel.”

# END OF SECTION 624