SECTION 712 - MISCELLANEOUS

Make the following amendment to said Section:

(I)	Amend 712.55(A)     General by revising the fourth paragraph to read as follows:

“Reflective thermoplastic compound pavement markings shall be alkyd-based.     Hydrocarbon based reflective thermoplastic compound pavement markings shall not be used.     The compound shall not deteriorate by contact with sodium chloride,  calcium chloride, oil content of pavement materials, or from oil droppings from traffic.”

# END OF SUBSECTION 712.55