SECTION 712 - MISCELLANEOUS

Make the following amendment to said Section:

(I)	Amend 712.30     Mast Arms to read as follows:

“712.30	Luminaire Mast Arms.     Upswept steel or seamless aluminum tube mast arms shall be furnished of specified size, length, and rise for installation on poles.     Tapered elliptical self-supporting mast arms shall be furnished for mast arm lengths shorter than ten feet and truss type mast arms for mast arm lengths equal to or greater than ten feet.     Mast arms shall be furnished that can support equipment shown in the plans and that are capable of withstanding 100 miles per hour winds average and 110 miles per hour gusts.     Ends of mast arms shall be completed in two-inch slipfitter with inner-wired type pole plates.     The Engineer will not permit mixture of pole materials.”

# END OF SECTION 712