SECTION 202 – REMOVAL OF STRUCTURES AND OBSTRUCTIONS

Make the following amendments to said Section:

(I)	Amend 202.04 – Measurement by revising lines 119 to 120 to read as follows:

“202.04	Measurement.  If the proposal provides a contract item for the removal of structure and obstructions, the Engineer will measure the removal of structures and obstructions by the square yard, each, or linear foot.

The Engineer will not measure the removal of structures and obstructions when contracted on a lump sum basis.”

(II)	Amend 202.05 – Payment by revising lines 122 to 131 to read as follows:

“202.05	Payment.  If the proposal does not show a contract item for the removal of structures and obstructions, the Engineer will not pay for the removal of structures and obstructions separately.  The Contractor shall consider them incidental to the various contract items.

The Engineer will pay for specific items stipulated for removal and disposal at the contract price bid per unit specified in the proposal.  The price shall be full compensation for removal and disposal of that items, excavation, backfill, salvage of materials removed.  Salvaging of materials removed includes their custody, preservation, storage on the right-of-way.  Also, the price shall be full compensation for equipment, tools, labor materials and incidentals necessary to complete the work.

The Engineer will pay for the following pay item when included in the proposal schedule.

Pay Item	Pay Unit

Removal of __________________	Lump Sum

Removal of __________________	Each

Removal of __________________	Linear Foot

Removal of __________________					Square Yard”

# END OF SECTION 202