SECTION 502 - TIMBER STRUCTURES

Make the following amendments to said Section:

(I)	Amend 502.04 – Measurement by revising lines 353 to 354 to read as follows:

“502.04	Measurement.  The Engineer will measure the timber incorporated into the structure by the thousand feet board measure (MFBM).  The Engineer will base the computation of the quantity of lumber or timber in the structure on nominal sizes and the shortest commercial lengths that the Contractor can use.  Short pieces of odd lengths from longer commercial lengths will be the exception.

The Engineer will not measure timber when contracted on a lump sum basis.”

(II)	Amend 502.05 – Payment by revising lines 356 to 375 to read as follows:

“502.05	Payment.  The Engineer will pay for the accepted quantities of timber at the contract unit price per thousand feet board measure or at the contract lump sum price for each pay item listed below and contained in the proposal.  The price paid shall be full compensation for furnishing, delivering, preparing, framing, assembling, building, and painting timbers and lumbers; for other materials for the complete structure; and for labor, equipment, tools, and incidentals necessary to complete the structure.

The Engineer will pay for the following pay items when included in the proposal schedule:

Pay Item	Pay Unit

Untreated Timber	MFBM

Untreated Timber	Lump Sum

Treated Timber	MFBM

Treated Timber	Lump Sum

The Engineer will not pay for timber bumpers at ends of concrete floor slabs and will consider cost for timber bumpers at ends of concrete floor slabs as included in the contract prices for untreated and treated timber.  Cost is for work prescribed in this section and the contract documents.

The Engineer will pay for timber piling in accordance with and under Section 505 - Piling.”

### END OF SECTION 502