SECTION 603 – CULVERTS AND STORM DRAINS

Make the following amendments to said Section:

(I)	Amend 603.03(C)(1) - Culverts by revising lines 106 to 108 to read as follows:

“Spacing between multi-barrel culverts shall be a minimum of 18 inches or 0.5 the culvert width, whichever is greater.  The minimum spacing shall be 1 foot when placing controlled low strength material (CLSM) as backfill. Anchor the culverts in such a manner that the horizontal and vertical alignment of the culverts does not change.”

(II)	Amend 603.04 – Measurement by revising lines 282 to 292 to read as follows:

“603.04	Measurement.

(A)	The Engineer will measure bed course material for culverts per cubic yard in accordance with contract documents.

(B)		The Engineer will measure reinforced concrete collar per each in accordance with contract documents.

(C)	The Engineer will measure reinforced concrete pipe, spiral rib aluminum pipe, high density polyethylene pipe, corrugated steel pipe, corrugated pipe arch, structural plate, and reinforced concrete jacket per linear foot in accordance with contract documents.

(D)	The Engineer will measure cleaning of existing culverts on a force account basis in accordance with Subsection 109.06 - Force Account Provisions and Compensation and as ordered by the Engineer.”

(III)	Amend 603.05 – Payment by revising lines 294 to 349 to read as follows:

“603.05	Payment.  The Engineer will pay for the accepted pay items listed below at the contract price per pay unit, as shown in the proposal schedule.  Payment will be full compensation for the work prescribed in this section and contract documents.

The Engineer will pay for each of the following pay items when included in the proposal schedule:

# Pay Item	Pay Unit

Bed Course Material for Culvert	Cubic Yard

_____ - Inch Reinforced Concrete Pipe, Class _____	Linear Foot

_____ - Inch Spiral Rib Aluminum Pipe, Sheet Thickness,

_____ - Inch	Linear Foot

_____ - Inch High Density Polyethylene Pipe, Type _____	Linear Foot

_____ - Inch Corrugated __________, Sheet Thickness,

_____ - Inch	Linear Foot

_____ - Inch Reinforced Concrete Pipe, Class _____, or

_____ - Inch High Density Polyethylene Pipe, Type _____, or

_____ - Inch Corrugated Steel Pipe, Sheet Thickness

_____ - Inch, or

_____ - Inch Spiral Rib Aluminum Pipe, Sheet Thickness,

_____ - Inch	Linear Foot

_____ - Inch Reinforced Concrete Pipe, Class _____, or

_____ - Inch High Density Polyethylene Pipe, Type _____, or

_____ - Inch Spiral Rib Aluminum Pipe, Sheet Thickness,

_____ - Inch,	Linear Foot

_____ - Inch Reinforced Concrete Pipe, Class _____, or

_____ - Inch High Density Polyethylene Pipe, Type _____	Linear Foot

_____ - Inch Reinforced Concrete Pipe, Class _____, or

_____ - Inch Spiral Rib Aluminum Pipe, Sheet Thickness,

_____ - Inch 	Linear Foot

_____ - Corrugated ______ Pipe Arch, Sheet Thickness,

_____ - Inch 	Linear Foot

_____ - Inch Structural _____ Plate _____, No. _____ Gage	Linear Foot

_____ - Inch Structural Steel Plate _____, No. _____ Gage, or

_____ - Inch Structural Aluminum Plate _____, No._____ Gage	Linear Foot

Reinforced Concrete Collar ______	Each

Reinforced Concrete Jacket ______	Linear Foot

(1)	100 percent of contract bid price upon completion of constructing concrete jacket.

Clean Existing Culverts	Force Account”

# END OF SECTION 603