SECTION 606 – GUARDRAIL

Make the following amendment to said Section:

(I)   Amend 606.04 - Measurement by replacing lines 116 to 118 to read:

“606.04   	Measurement.  The Engineer will measure guardrail per linear foot in accordance with the contract documents.

The Engineer will measure from center to center of end posts.  If the Contractor makes end connections to masonry or steel structures, the Engineer will measure to the face of such structures.

The Engineer will measure rigid barrier type guardrail per linear foot from end to end of the type specified.

The Engineer may measure end anchorage, terminal section and transition section:

- as units of each kind when specified in the proposal or

- include in the quantities of guardrail of the respective type and not measured separately

The Engineer will measure resetting existing guardrail per linear foot from end to end.”

(II)	Amend 606.05 – Payment by revising lines 120 to 138 to read as follows:

“606.05	Payment.	The Engineer will pay for the accepted pay items listed below at contract price per pay unit, as shown in the proposal schedule.  Payment will be full compensation for the work prescribed in this section and the contract documents.

The Engineer will pay for the following pay items when included in the proposal schedule:

Pay Item									       Pay Unit

Guardrail Type ____							   Linear Foot

End Anchorage Type ____								  Each

Terminal Section Type ____							  Each

Transition Section Type ____							  Each

Reset Guardrail								  Linear Foot”

# END OF SECTION 606