SECTION 613 – CENTERLINE AND REFERENCE SURVEY MONUMENTS

Make the following amendments to said Section:

(I)	Amend Subsection 613.03(A) – Initial Installation from lines 22 to 26 to read:

“(A)	Initial Installation.     Cut holes, in completed medians and shoulders,  to required depth or to solid rock, whichever is less.     Fill hole with concrete.     Burr or feather plug for anchorage in concrete.     Place the 4 #4 x 20-inch bars as shown on the plans when curing the concrete.     Install brass plug in required position after concrete has sufficiently set.     After curing concrete at least 7 days, restore edge of pavement surrounding monument to original condition.”

(II)	Amend 613.04 – Measurement by revising lines 48 to 56 to read as follows:

“613.04	Measurement.

- New centerline and reference survey monuments and reconstructing centerline and reference survey monuments will be paid on a lump sum basis.  Measurement for payment will not apply.

The Engineer will measure adjusting centerline and reference survey monuments per each in accordance with the contract documents.

- The Engineer will measure new centerline and reference survey monuments, reconstructing centerline and reference survey monuments, and adjusting centerline and reference survey monuments per each in accordance with the contract documents.”

(III)	Amend 613.05 – Payment by revising lines 62 to 79 to read as follows:

“613.05	Payment.

- The Engineer will pay for the accepted new centerline and reference survey monuments and reconstructing centerline and reference survey monuments on a contract lump sum basis.  The Engineer will pay for the accepted adjusting centerline and reference survey monument at the contract unit price per each.  Payment will be full compensation for work prescribed in this section and the contract documents.

- The Engineer will pay for the accepted new centerline and reference survey monuments, reconstructing centerline and reference survey monuments, and adjusting centerline and reference survey monuments at the contract unit price per each.  Payment will be full compensation for work prescribed in this section and the contract documents.

The Engineer will pay for each of the following pay items when included in the proposal schedule:

Pay Item							       Pay Unit

(A)	Centerline and Reference Survey Monuments		   	    Lump Sum

Reconstructing Centerline and Reference

Survey Monuments	 					    	    Lump Sum

(B)	Centerline and Reference Survey Monuments				  Each

Reconstructing Centerline and Reference Survey Monuments	 Each”

# END OF SECTION 613