SECTION 628 – SHOTCRETE

Make the following amendment to said Section:

(I)   Amend 628.04 - Measurement by replacing lines 344 to 345 to read:

“628.04	Measurement.  The engineer will measure the shotcrete by the cubic yard or square yard complete in place as specified in the proposal.  The Engineer will compute the actual yardage within the neat lines and dimensions of the structure shown in the contract or ordered by the Engineer.”

(II)	Amend 628.05 – Payment by revising lines 347 to 359 to read as follows:

“628.05	Payment.  The Engineer will pay for the accepted quantities of shotcrete at the contract unit price per cubic yard or square yard as specified in the proposal.

Payment will be full compensation for the work prescribed in this section and the contract documents.

The Engineer will pay for the following pay item when included in the proposal schedule:

Pay Item	Pay Unit

Shotcrete for		Cubic Yard

Shotcrete for _________________		Square Yard

The Engineer will pay for reinforcing steel in accordance with and under Section 602 - Reinforcing Steel.”

# END OF SECTION 628