SECTION 630 – TRAFFIC CONTROL GUIDE SIGNS

Make the following amendment to said Section:

- Amend Section 630.02 - Materials, by replacing lines 28 to 29 to read:

“Retroreflective sheeting shall conform to criteria listed in ASTM D 4956 for the applicable type and class, or as amended in accordance with Subsection 750.01 - Signs.”

- Amend Section 630.04 - Measurement, by replacing lines 204 to 221 to read:

“630.04	Measurement.  The Engineer will measure destination, expressway, directional and exit number sign panels by the square foot of sign face.

The Engineer will measure destination and ground mounted expressway sign (“E” Designation) posts by the linear foot.

The Engineer will measure overhead mounted expressway sign (“E” designation) post and arm posts per each as complete units of the type and design specified in the proposal.

The engineer will measure directional sign (“DIR” designation) posts per each, complete in place.

The Engineer will measure the number of route markers assemblies as complete units of the type and design specified in the proposal.

The Engineer will measure the footings for destination and ground mounted expressway signs (“E” designation) as complete units for each type of footing as specified in the proposal.

Measurement of contract items for construction of footings for overhead mounted expressway signs will be as follows:

- The Engineer will measure excavation according to Section 204 – Excavation and Backfill for Miscellaneous Facilities.

- The Engineer will measure concrete according to Section 503 – Concrete Structures.

- The Engineer will measure reinforcing steel according to Section 602 – Reinforcing Steel.

When the Engineer accepts an alternative design, the method of measurement for the various contract items affected by the design shall be identical with the various original contract items shown in the contract.  The Engineer will not measure the additional items that the Contractor requires for the alternate design.

The Engineer will not measure removal and disposal and storing of existing and temporary signs and markers that the Contractor will not incorporate in the completed highway for payment.”

(III)	Amend 630.05 – Payment by revising lines 223 to 303 to read as follows:

“630.05	Payment.  The Engineer will pay for destination, expressway, directional and exit number sign panels at the contract price per square foot for the type specified complete in place.  Payment will be full compensation for the work prescribed in this section and the contract documents.

The Engineer will pay for destination and ground mounted expressway sign (“E” designation) posts at the contract price per linear foot for the type specified complete in place.  Payment will be full compensation for the work prescribed in this section and the contract documents.

The Engineer will pay for overhead mounted expressway sign (“E” designation) post and arm at the contract price per each type as specified complete in place.  Payment will be full compensation for the work prescribed in this section and the contract documents.

The Engineer will pay for directional sign (“DIR” designation) posts at the contract price per each for the type specified complete in place.  Payment shall be full compensation for the work prescribed in this section and the contract documents.

The Engineer will pay for route marker assemblies at the contract price per each for the type and design specified complete in place.  Payment will be full compensation for the work prescribed in this section and the contract documents.

The Engineer will pay for footings for destination and ground mounted expressway signs (“E” designation) at the contract price per each, complete in place.  Payment will be full compensation for the work prescribed in this section and the contract documents.

The Engineer will not pay for removing and disposing or storing of existing and temporary signs that the Contractor will not incorporate in the completed highway separately.  The Engineer will consider them incidental to the various contract items.

The Engineer will not make payment other than those specified herein for the construction of footings for overhead mounted expressway signs.  The Engineer will pay for the work, materials, tools, equipment and incidentals required in the construction of the footings for overhead mounted expressway signs under the following contract items:

- Footing Excavation.  The Engineer will make payment for footing excavation according to Section 204 – Excavation and Backfill for Miscellaneous Facilities.

- Concrete.  The Engineer will make payment for concrete in footings according to Section 503 – Concrete Structures.

- Reinforcing Steel.  The Engineer will make payment for reinforcing steel according to Section 602 – Reinforcing Steel.

The Engineer will pay for the following pay items when included in the proposal schedule:

Pay Item	Pay Unit

Panel for ______	Square Foot

______ Post for ______	Linear Foot

Type _____ Post and Arms for _____	Each

Type _____ Route Marker Assembly	Each

Directional Sign Post	Each

Type _____ Footing for _____ Sign	Each

When the Engineer accepts an alternate design, the total amount paid shall be full compensation for furnishing and installing materials and furnishing equipment, tools, labors, and incidentals necessary to complete the work.  The Engineer will not make payment for additional materials, equipment, tools, labor and other incidentals that might become necessary to complete the installation due to the alternate design.

# END OF SECTION 630