SECTION 638 – PORTLAND CEMENT CONCRETE CURB AND GUTTER

Make the following amendments to said Section:

(I)	Amend 638.04 – Measurement by revising lines 130 to 131 to read as follows:

“638.04	Measurement.  The Engineer will measure curb and/or gutter, both new and reset, by the linear foot.  The Engineer will measure along the front face of the curb at the finished grade elevation.  If the Engineer measures gutter separately, the Engineer will measure gutter along the front face of the gutter.  The Engineer will not make deduction in gutter length for drainage appurtenances installed such as catch basins and drop inlets.

The Engineer will not measure curb and/or gutter both new and reset when contracted on a lump sum basis.

The Engineer will measure curb and/or gutter transition for payment as follows:

| From | To | Measurement for Payment |
| --- | --- | --- |
| Cast-in-place Curb or Precast Curb | Cast-in-place Curb and Gutter | Cast-in-place Curb and Gutter |
| Cast-in-place Curb and Gutter | Precast Curb and Cast-in-place Gutter | Cast-in-place Curb and Gutter |
| Cast-in-place Curb and Gutter Type _____ | Cast-in-place Curb and Gutter Type _____ | Cast-in-place Curb and Gutter 1/2 of Transition to each type |
| Cast-in-place Curb Type _____ | Cast-in-place Curb Type _____ | Cast-in-place Curb 1/2 of Transition to each type |

The Engineer will measure precast concrete drop curb and driveway curb or cast-in-place integral driveway curb and gutter under the adjacent normal curb and/or gutter.”

(II)	Amend 638.05 – Payment by revising lines 133 to 148 to read as follows:

“638.05	Payment.  The Engineer will pay for the accepted quantities of curb and/or gutter at the contract lump sum price or at the contract unit price per linear foot for each type of curb and/or gutter specified.

Payment will be full compensation for work prescribed in this section and contract documents.

The Engineer will pay for each of the following pay items when included in proposal schedule:

# Pay Item					Pay Unit

Curb, Type _____	Linear Foot,

Lump Sum

Gutter, Type _____	Linear Foot,

Lump Sum

Curb and Gutter, Type _____	Linear Foot,

Lump Sum

Reset Curb, Type _____	Linear Foot,

Lump Sum”

### END OF SECTION 638