Make the following amendment to said Section:

SECTION 106 – MATERIAL RESTRICTIONS AND REQUIREMENTS

(I)	Amend 106.05(B) – Deviation by revising the third sentence from line 106 to 108 to read as follows:

“Any deviations will be subject to Subsection 102.14 – Substitution of Materials and Equipment Before Bid Opening.

(II)	Amend Section 106 – Material Restrictions and Requirements by adding the following after line 334

106.14	Construction Materials.

(A)	Buy America requirements apply to the following construction materials if permanently incorporated into the project unless otherwise specified:

- Non-ferrous metals.

- Plastic and polymer-based products such as:

- High Density Polyethylene

- Polyvinylchloride.

- Composite building materials.

- Polymers used in fiber optic cables.

- Glass (including optic glass).

- Fiber optic cable (including drop cable).

- Optical fiber.

- Lumber.

- Engineered wood.

- Drywall.

- Manufactured products containing steel and iron material

Where one or more of these construction materials have been combined by a manufacturer with other materials through a manufacturing process,  Buy America requirements do not apply unless otherwise specified.  Furnish construction materials to be incorporated into the work with certificates of compliance with each project delivery.  Manufacturer’s certificate of compliance must identify where the construction material was manufactured and attest specifically to Buy America compliance.  All manufacturing processes for these materials must occur in the United States.

Non-ferrous metals, such as aluminum, copper, lead, nickel, tin, titanium, zinc, brass, and bronze, are subject to Buy America requirements if used as construction materials in various shapes, sizes, and gauges including channels, bars, pipe, couplers, fittings, bolts, nuts, and products made of 100 percent of the non-ferrous metal.  If the non-ferrous metal is combined with other construction materials during a manufacturing process, the product is considered a manufactured product and not subject to Buy America requirements.

One hundred percent plastic or polymer materials are subject to Buy America requirements.  This includes high-density polyethylene or polyvinyl chloride pipe and fittings.  Plastics or polymers that are combined with other construction materials in a manufacturing process are considered a manufactured product and not subject to these requirements.

Glass construction materials subject to Buy America requirements are composed solely of glass.  This includes glass beads incorporated into pavement striping and 100 percent Fiberglass material.

Fiber optic cable (including drop cable) and optical fiber are subject to Buy America requirements.

Lumber products including engineered lumber are subject to Buy America requirements.

Manufactured products containing steel or iron including pre-cast concrete products are subject to Buy America requirements.

## END OF SECTION 106